## Slide 1
UR5 搭载 D405 的生物实验视觉定位数据流
从 RGB-D 采集到物体在机器人基坐标系下的三维重心，配置参数作为外部先验接入对应处理环节。
中文流程图
D405 采集参数
30 帧预热 / 10 帧采集
深度对齐到彩色流
↓
视觉模型配置
VL_MODE=api：Qwen3-VL-30B-A3B-Instruct
SAM2.1 Hiera Tiny，CUDA
↓
相机内参与深度尺度
fx=fy=663.6542
Depth scale=1e-4，Z×1.005
↓
机器人与手眼标定
UR5 TCP 30003
T_cam_to_end 4×4
↓
STEP 1
相机拍摄
获取同一时刻、同一视角下的彩色图和深度图
RealSense pipeline 启动
预热帧：Temporal Filter 稳定深度
采集多帧 RGB-D
深度帧做时间滤波
多帧深度取中值
RGB-D 对齐到 color stream
输入：实验台场景
输出：color.jpg + depth.png
STEP 2
VLM 识别
把目标物体从图像中定位为候选框
Agent 输入固定/终端 prompt
API 模型：Qwen3-VL-30B-A3B
或本地 Qwen3-VL 8B
输出 0-1000 归一化框
解析为像素坐标
过滤面积 < 3000 px 的框
输入：color.jpg
输出：目标名 + bbox
STEP 3
SAM2 分割
将粗框细化为可用于深度裁剪的像素级 mask
SAM2ImagePredictor.set_image
bbox 作为 box prompt
SAM2.1 Hiera Tiny 预测 mask
形态学开运算 ×2
形态学闭运算 ×1
连通域 < 500 px 删除
GaussianBlur σ=3 平滑
输入：color.jpg + bbox
输出：bool mask + overlay
STEP 4
点云重建
把目标 mask 内深度转换为相机坐标系点云并求重心
depth / 10000 × 1.005 得 z
由 D405 内参反投影到 (x,y,z)
mask 裁剪目标点云
体素降采样 1 mm
统计离群滤波：20 邻域, 1.5σ
PCA 求 OBB 与最短边
输入：depth.png + mask
输出：目标点云 + OBB
STEP 5
坐标变换
把相机坐标重心转换到 UR5 基坐标系供操作规划使用
自适应 DBSCAN：eps=0.1×OBB 最短边
保留最大簇，可保留达 50% 的第二大簇
OBB 中心区域均值作为重心
UR pose 用 Rodrigues 转 T_end_base
P_base = T_end_base · T_cam_end · P_cam
写入 vision_result.txt
输入：相机系重心 P_cam
输出：基坐标系 [x,y,z]
→
RGB-D 文件
→
候选框
→
目标 mask
→
3D 重心
图例
绿色：模块输入
蓝色：模块输出
黄色：config.py 先验/标定
Debug 模式还会保存 VLM 检测图、SAM overlay/mask、Open3D 点云截图和 2×2 报告图；experiment 模式只输出终端与 result/vision_result.txt。

## Slide 2
UR5-mounted D405 vision localization pipeline for biological experiments
The pipeline converts one RGB-D observation into object centroids in the robot base frame; config.py supplies calibration and model priors.
English flowchart
D405 capture settings
30 warm-up / 10 collection frames
Depth aligned to color
↓
Vision model settings
VL_MODE=api: Qwen3-VL-30B-A3B-Instruct
SAM2.1 Hiera Tiny on CUDA
↓
Camera intrinsics + depth scale
fx=fy=663.6542
Depth scale=1e-4, Z×1.005
↓
Robot and hand-eye calibration
UR5 TCP 30003
T_cam_to_end 4×4
↓
STEP 1
RGB-D Capture
Acquire synchronized color and depth images from the lab bench.
Start RealSense pipeline
Warm up temporal depth filter
Collect multiple RGB-D frames
Apply temporal filtering to depth
Median-filter the collected depth stack
Align depth to color stream
Input: bench scene
Output: color.jpg + depth.png
STEP 2
VLM Detection
Localize target lab objects as coarse candidate boxes.
Agent sends fixed or terminal prompt
API: Qwen3-VL-30B-A3B
or local Qwen3-VL 8B
Return normalized 0-1000 boxes
Parse boxes into pixel coordinates
Reject boxes < 3000 px
Input: color.jpg
Output: object name + bbox
STEP 3
SAM2 Segmentation
Refine each coarse box into a pixel mask for depth cropping.
SAM2ImagePredictor.set_image
Use bbox as the box prompt
SAM2.1 Hiera Tiny predicts mask
Morphological opening ×2
Morphological closing ×1
Remove components < 500 px
Gaussian smoothing, σ=3
Input: color.jpg + bbox
Output: bool mask + overlay
STEP 4
Point-cloud Reconstruction
Convert masked depth into camera-frame point clouds and centroids.
z = depth / 10000 × 1.005
Back-project with D405 intrinsics
Crop object points by mask
Voxel downsample at 1 mm
Statistical outlier removal: 20-NN, 1.5σ
PCA estimates OBB and shortest axis
Input: depth.png + mask
Output: object cloud + OBB
STEP 5
Coordinate Transform
Transform camera-frame centroids into the UR5 base frame.
Adaptive DBSCAN: eps=0.1×shortest OBB axis
Keep largest cluster; keep top-2 if second ≥50%
Centroid = mean after OBB-centered trimming
Convert UR pose to T_end_base via Rodrigues
P_base = T_end_base · T_cam_end · P_cam
Write vision_result.txt
Input: camera-frame centroid
Output: base-frame [x,y,z]
→
RGB-D files
→
boxes
→
masks
→
3D centroids
Legend
Green: module input
Blue: module output
Yellow: config.py prior/calibration
Debug mode also saves VLM detections, SAM overlays/masks, Open3D point-cloud screenshots, and a 2×2 report; experiment mode keeps terminal output and result/vision_result.txt.